## Slide 1: A uGNI-Based Asynchronous Message-driven Runtime System for Cray Supercomputers with Gemini Interconnect
Yanhua Sun, Gengbin Zheng, Laximant(Sanjay) Kale
Parallel Programming Lab
University of Illinois at Urbana-Champaign
Ryan Olson, Cray Inc
Terry R. Jones, Oak Ridge National Lab
26th IEEE International Parallel & Distributed Processing Symposium

## Slide 2: Motivation
Modern interconnects are complex
Multiple programming models/languages are developed

## Slide 3: Motivation
Modern interconnects are complex
Multiple programming models/languages are developed
How to attain good performance for applications in alternative models on different interconnects ?

## Slide 4: Motivation
Modern interconnects are complex
Multiple programming models/languages are developed
How to attain good performance for applications in alternative models on different interconnects ?
Charm++ programming model on Gemini Interconnect
Notes: For example NQueens

## Slide 5: Outline
Overview of Charm++, Gemini and uGNI
Design of uGNI-based Charm++
Optimizations to improve communication
Micro-benchmark and application results

## Slide 6: Charm++ Software Architecture
  Charm++ is an
  object-based over decomposition programming model
  Adaptive intelligent runtime
    dynamic load balancing
    fault tolerance
  Scales to 300K cores
  Portable
  Run on MPI

## Slide 7: Gemini Interconnect
  Low latency (700ns)
  High bandwidth (8GBytes/sec)
  Scale to 100,000 nodes
Notes: Framework . User do not need to know any of these problems and techniques

## Slide 8: Gemini Interconnect
  Low latency (700ns)
  High bandwidth (8GBytes/sec)
  Scale to 100,000 nodes
  Hardware support for one-sided communication
  Fast Memory Access (FMA)
  Block Transfer Engine (BTE)
Notes: Framework . User do not need to know any of these problems and techniques

## Slide 9: uGNI
User-level Generic Network Interface
  Memory Registration/de-
  Post FMA/BTE transactions
  Completion Queues

## Slide 10: Initial Pingpong Performance
Notes:   Unnecessary features in MPI lead to overhead
  Data interaction pattern in Charm++ is different from MP : Only sender-involving

## Slide 11: Design of uGNI-based Charm++
  Small messages (less than 1024 bytes)
  SMSG directly send with data_tag

## Slide 12: Baseline Pingpong Performance

## Slide 13: Persistent Messages
Communication with fixed pattern
  Communication processors
  Data size
Re-use memory
  Avoid memory allocation
  Avoid the first handshake message

## Slide 14: Persistent Messages
Baseline design to transfer data
Transfer persistent messages

## Slide 15: Persistent Messages Performance

## Slide 16: Memory Pool
Memory registration/de-registration costs a lot
Charm++ controls all memory allocation/de-allocation

## Slide 17: Memory Pool
Memory registration/de-registration costs a lot
Charm++ controls all memory allocation/de-allocation
Pre-alloc/register big chucks of memory
Allocation/de- is from memory pool

## Slide 18: Performance of Memory Pool

## Slide 19: Performance – Message Latency

## Slide 20: Performance - Bandwidth

## Slide 21: NQueens (fine-grained)

## Slide 22: NAMD Performance

## Slide 23: NAMD 100M-atom on Titan
32%
70% efficiency
17%

## Slide 24: Conclusion
Gemini Interconnect, Charm++
Optimizations
  Persistent messages
  Memory pool
Micro-benchmark and application results
http://charm.cs.uiuc.edu/software